# SECTION 1200

MISCELLANEOUS CONSTRUCTION

SECTION 1201 – TOPSOIL

1201-1  DESCRIPTION

This item shall consist of preparing the ground surface for topsoil application, removing topsoil from designated stockpiles or areas to be stripped on the site or from approved sources off the site, and placing and spreading the topsoil on prepared areas in accordance with this specification at the locations shown on the plans as directed by the ENGINEER.

1201-2  MATERIALS

1201-2.1  TOPSOIL.  Topsoil shall be the surface layer of soil with no admixture of refuse or any material toxic to plant growth, and it shall be reasonably free from subsoil and stumps, roots, brush, stones (2 inches or more in diameter), clay lumps, or similar objects.  Brush and other vegetation which will not be incorporated with the soil during handling operations shall be cut and removed.  Ordinary sods and herbaceous growth such as grass and weeds are not to be removed but shall be thoroughly broken up and intermixed with the soil during handling operations.  The topsoil or soil mixture, unless otherwise specified or approved, shall have a pH range of approximately 5.5 pH to 7.6 pH, when tested in accordance with the methods of testing of the Association of Official Agricultural Chemists in effect on the date of invitation of bids.  The organic content shall be not less than 3 percent nor more than 20 percent as determined by the wet-combustion method (Chromic acid reduction).  There shall be not less than 20 percent nor more than 80 percent of the material passing the 200 mesh sieve as determined by the wash test in accordance with ASTM D1140.

Natural topsoil may be amended by the CONTRACTOR with approved materials and methods to meet the above specifications.

1201-2.2  Inspection and Tests.  Within ten (10) days following acceptance of the bid, the ENGINEER shall be notified of the source of topsoil to be furnished by the CONTRACTOR.  The topsoil shall be inspected to determine if the selected soil meets the requirements specified and to determine the depth to which stripping will be permitted.  At this time, the CONTRACTOR may be required to take representative soil samples from several locations within the area under consideration and to the proposed stripping depths, for testing purposes as specified in 1201-2.1.

1201-3  CONSTRUCTION REQUIREMENTS

1201-3.1  GENERAL.  Areas to be topsoiled shall be shown on the plans.  If topsoil is available on the site, the location of the stockpiles or areas to be stripped of topsoil and the stripping depths shall be shown on the plans.

Suitable equipment necessary for proper preparation and treatment of the ground surface, stripping of topsoil, and for the handling and placing of all required materials shall be on hand, in good condition, and approved by the ENGINEER before the various operations are started.

1201-3.2  Preparing the Ground Surface.  Immediately prior to dumping and spreading the topsoil on any area, the surface shall be loosened by disks or spike-tooth harrows, or by other means approved by the ENGINEER, to a minimum depth of 2 inches to facilitate bonding of the topsoil to the covered subgrade soil.  The surface of the area to be topsoiled shall be cleared of all stones larger than 2 inches in any diameter, and all litter or other material which may be detrimental to proper bonding, the rise of areas, as shown on the plans, which are too compact to respond to these operations shall receive special scarification.

Grades on the area to be topsoiled, which have been established by others as shown on the plans, shall be maintained in a true and even condition.  Where grades have not been established, the areas shall be smooth-graded and the surface left at the prescribed grades in an even and properly compacted condition to prevent, insofar as practical, the formation of low places or where water will stand.

1201-3.3  Obtaining Topsoil.  Prior to the stripping of topsoil from designated areas, any vegetation, briers, stumps and large roots, rubbish, or stones found on such areas, which may interfere with subsequent operations, shall be removed using methods approved by the ENGINEER.  Heavy sod or other cover, which cannot be incorporated into the topsoil by disking or other means, shall be removed.

When suitable topsoil is available on the site, the CONTRACTOR shall remove this material from the designated areas and to the depth as directed by the ENGINEER.  The topsoil shall be spread on areas already tilled and smooth graded, or stockpiled in areas approved by the ENGINEER.  Any topsoil stockpiled by the CONTRACTOR shall be rehandled and placed without additional compensation.  Any topsoil that has been stockpiled on the site by others and is required for topsoiling purposes, shall be removed and placed by the CONTRACTOR.  The sites of all stockpiles and areas adjacent thereto, which have been disturbed by the CONTRACTOR, shall be graded if required and put into a condition acceptable for seeding.

When suitable topsoil is secured off the project site, the CONTRACTOR shall locate and obtain the supply, subject to the approval of the ENGINEER.  The CONTRACTOR shall notify the ENGINEER sufficiently in advance of operations in order that necessary measurements and tests can be made.  The CONTRACTOR shall remove the topsoil from approved areas and to the depth as directed.  The topsoil shall be hauled to the site of the work and placed for spreading or spread as required.  Any topsoil hauled to the site of the work and stockpiled shall be rehandled and placed without additional compensation.

1201-3.4  Placing Topsoil.  The topsoil shall be evenly spread on the prepared areas to a uniform depth of 4 inches after compaction unless otherwise shown on the plans or stated in the special provisions.  Spreading shall not be done when the ground or topsoil is frozen, excessively wet, or otherwise in a condition detrimental to the work. Spreading shall be carried on so that turfing operations can proceed with a minimum of soil preparation or tilling.

After spreading, any large, stiff clods and hard lumps shall be broken with a pulverizer or by other effective means, and all stones or rocks (2 inches or more in diameter), roots, litter, or any foreign matter shall be raked up and disposed of by the CONTRACTOR.  After spreading is completed, the topsoil shall be satisfactorily compacted by rolling with a cultipacker or by other means approved by the ENGINEER. The compacted topsoil surface shall conform to the required lines, grades, and cross sections.  Any topsoil or other dirt falling upon pavements as a result of hauling or handling of topsoil shall be promptly removed.

1201-4  MEASUREMENT AND PAYMENT

1201-4.1  Topsoiling.  Topsoiling shall be measured by the cubic yard (CY) and paid for at the unit price bid for "Topsoiling" complete in place and accepted by the ENGINEER.  When topsoil is weighed for final quantity, it shall be converted to cubic yards at the rate of 1.3 tons per cubic yard or at a rate approved by the ENGINEER.