SECTION 300

BASE COURSES

# SECTION 301 – SAND SUBBASE

301-1  DESCRIPTION

This item shall consist of sand subbase course constructed on a prepared subgrade or underlying course in accordance with these specifications and in conformity with the dimensions and typical cross section shown on the plans and with the lines and grades established by the ENGINEER.

301-2  MATERIALS

The sand to be furnished under this item shall conform to Subsection 501-2.5 of these specifications.

301-3  CONSTRUCTION REQUIREMENTS

Sand subbase shall be placed, spread, shaped, and compacted prior to the placement of the pavement, sidewalk, curb, and gutter, etc.  The sand subbase shall be compacted by at least two (2) complete passes over the entire width of the forms by a vibratory compactor.  Immediately prior to concrete placement, the sand subbase shall be regraded and watered thoroughly to produce a uniform wet appearance.

301-4  MEASUREMENT AND PAYMENT

301-4.1  sand subbase.  Sand subbase shall be measured by the ton and paid for at the unit price bid for "Sand Subbase."  Water used as specified above shall be considered incidental to the "Sand Subbase" item and separate payment shall not be made for watering.