SECTION 406 – ASPHALT REMOVAL

  - DESCRIPTION

This work consists of removing, and disposing of, existing AC pavement surfacing.

  - EQUIPMENT

The CONTRACTOR shall use a saw, milling wheel, or asphalt cutting wheel to make all pavement cuts.  The CONTRACTOR shall furnish all equipment for cutting, removing, loading, and hauling removed asphalt to the designated unloading site.

  - CONSTRUCTION REQUIREMENTS

All asphalt cuts shall be made to maintain a vertical face on the remaining asphalt which shall be maintained until the pavement is replaced and accepted by the ENGINEER.  Pavement cuts shall be as designated on plans or as marked by the ENGINEER.  Any removal and replacement beyond the area specified on plans or marked by the ENGINEER shall be the responsibility of the CONTRACTOR to replace.

Pavement removed shall be salvaged as clean as practical, delivered to the "City of Watford City Storage Facility located at 1101 South 14th Street, and stockpiled in large piles.  It shall be considered incidental to the price bid for "Pavement Removal."  Landfill fees shall be waived for clean asphalt.

Protection of adjacent pavements shall be the responsibility of the CONTRACTOR.  A mutual inspection of the surrounding pavements shall be made, and any damages shall be repaired by the CONTRACTOR at no additional cost.

  - MEASUREMENT AND PAYMENT

406-4.1  ASPHALT REMOVAL.  Asphalt Removal shall be measured and paid by the square yard (SY) complete, disposed of properly, and accepted by the ENGINEER.  Replacement shall not be part of this bid item.